## Slide 1
EXPECTATIONS NFPA 1720
“Rural” Definition: Less than 500 people per square mile - 14 minutes – 6 FF – 80% of the time (RUSH) Last year it was 11.2 minutes
“Remote” Definition – More than 8 miles from station - 4 FF 90% of the time – no time requirement. (End of the road IOWA)

## Slide 2
IT IS TIME TO RETHINK HOW WE FIGHT FIRES!
limited staffing is a reality for many FD. Firefighters find themselves leaving the station with two firefighters aboard. Put the fire out FIRST, everything gets better after that takes place. Can you hit the fire from the outside?
The new research demonstrates that our fears of pushing fire by way of a window attack are unfounded. The fire is actually following the flow path we created when we opened the door, knock out large windows and make large ventilation holes in the roof of the building.

## Slide 3
Fire needs AIR, FUEL & HEAT, Cutting off the AIR slows it down, Putting on WATER slows it down and may even put it out!
If we make a minimal opening to the window to attack the fire and do not create a flow path by adding other large ventilation openings such as opening doors, we are unlikely to push the fire or make the situation worse. We will likely knock down or "reset" the fire, buying us some time for additional personnel to arrive. Then do an interior attack for mop-up and overhaul. When you make the opening be ready to apply lots of foam/water!

## Slide 4: Emergency Scene
Firefighter safety must be top priority.
Tunnel vision kills firefighters.
Look at entire scene, not just the obvious.

## Slide 5: Ten Rules of Engagement for Structural Fire Fighting: - Acceptability of Risk - Risk Assessment

## Slide 6: 10 Rules of Engagement for Structural Fire Fighting Acceptability of Risk
All interior fire fighting involves an inherent risk.
No building or property is worth the life of a fire fighter.
Some risk is acceptable, in a measured and controlled manner.
No level of risk is acceptable where there is no potential to save lives or savable property.
Firefighters shall not be committed to interior offensive firefighting operations in abandoned or derelict buildings.

## Slide 7
All feasible measures shall be taken to limit or avoid risks through risk assessment by a qualified officer.
It is the responsibility of the Incident Commander to evaluate the level of risk in every situation.
Risk assessment is a continuous process for the entire duration of each incident.
If conditions change, and risk increases, change strategy and tactics.
10. No building or property is worth the life of a fire fighter.

## Slide 8
2-18-09 – NIOSH 107-page report released outlined a host of failures in the way the FD tackled the fire in June 2007.
Multiple chief officers serving in command roles in an uncoordinated manner
The lack of an established accountability system to track firefighters on scene
A RIC not being established
An ISO not being assigned
Fire and police department not working effectively together to control traffic and protect hose lines delivering water to the scene.
Formal incident command was never formally announced or transferred as ranking officers arrived on scene.
Fire attack operations at the loading dock (D-side) and the main showroom (A-side) of the store were directed by different chief officers and were not coordinated.

## Slide 9
“Two in and two out”
How to comply with this rule.
Limit the amount of personnel inside the structure!
IF THE AREA THAT YOU ARE WORKING IN COULD BE I.D.L.H. - You MUST use the TWO IN /TWO OUT rule!

## Slide 10
As with the OSHA "two-in-two-out" requirement, NFPA 1720 also states that if initial-attack personnel arrive to a situation where there is an immediate life threat, interior operations can commence with less than four personnel. However, the IC must make this decision using all available information. The primary and the only factor in the decision to attempt interior operations is the possibility of someone being trapped.

## Slide 11
Other recommendations from NFPA 1720 include:
1. One individual shall assume the role of incident commander.
2. Some type of accountability system shall be used.
3. At least four members should be assembled before any interior operations are initiated. Two firefighters should be available outside to assist the two inside.
4. There should be the capability of performing other needed activities including:
a) fire suppression;
b) search and rescue;
c) forcible entry;
d) ventilation;
e) preservation of property;
f) accountability of personnel;
g) rapid intervention crew;
h) other support activities, as needed.

## Slide 12
Pre Planning
Special Hazards
Closest water supply and flow
Access to location & water in winter, spring & fall
Ventilation points – pre-planned
Possible fire load or contents
Construction of building & age
Change of building use
Security & extinguishment systems?

## Slide 13
Building Construction and Pre-Planning!

## Slide 14: While performing size-up, the incident priorities are:
FIREFIGHTER SAFETY
CIVILIAN SAFETY
INCIDENT STABILIZATION
PROPERTY CONSERVATION
These priorities NEVER change and must be considered at every alarm!

## Slide 15
Size-up should answer:
What have we got? What is burning? Where can it go? What is exposed? How are we going to stop or contain it?

## Slide 16
Bedford Hills Firefighter trapped as roof collapses
A three-alarm fire in Bedford Hills gutted an unoccupied 3,000-square-foot ranch house burning for hours and injuring several firefighters, including one who was briefly trapped after the roof collapsed. "The house was well-engulfed, well-advanced upon our arrival," Up to 75 firefighters poured water on the four-bedroom house. A few hours after firefighters arrived the blaze was under control, but not before a roof collapse near the "tail end" of the operation. One firefighter who was trapped under he roof that fell had to be taken to the hospital with burns.
Aggressive or Stupid?

## Slide 17
A fire in a one-story ranch home in Texas claimed the lives of two fire fighters. Sustained high winds occurred during the incident. The winds caused a rapid change in the dynamics of the fire after the failure of a large section of glass in the rear of the house. They were fighting the fire against the wind. HAVE THE WIND AT YOUR BACK TO STAY ALIVE!

## Slide 18
Applying water from the exterior, into the upwind side of the structure can have a significant impact on controlling the fire prior to beginning interior operations. It should be made clear that in a wind-driven fire, it is most important to use the wind to your advantage and attack the fire from the upwind side of the structure, especially if the upwind side is the burned side. Interior operations need to be aware of potentially rapidly changing conditions.

## Slide 19
WHY DO WE VENTILATE?
Remove heat, smoke and gases
Make the atmosphere more people friendly
Better visibility for everyone
Allow quicker access to the fire
Must be done in a systematic, coordinated manner – NOT DONE COORRECTLY CAN GET YOU KILLED AND DO A LOT MORE PROPERTY DAMAGE….

## Slide 20
SAFETY CONCERNS WHEN DOING A SEARCH
Have a plan and follow it
Use the buddy system
Follow a pattern
Maintain communications
Make use of a hand line or rope

## Slide 22: Lighting the scene should be a priority!